## Slide 1: Parallel Programming Platforms
David Monismith
Cs599
Based on notes from Introduction to Parallel Programming, Second Ed., by A. Grama, A. Gupta, G. Karypis, and V. Kumar

## Slide 2: Introduction
Serial view of a computer
  Processor<--->Datapath<---->Memory
  Includes bottlenecks
Multiplicity
  Addressed by adding more processors, more datapaths, and more memory
  May be exposed to the programmer or hidden
  Programmers need details about how bottlenecks are addressed to be able to make use of architectural updates

## Slide 3: Implicit parallelism (Last Time)
Pipelining
Superscalar Execution
VLIW (Very Long Instruction Word) Processors (Not covered in detail)
SIMD Assembly Instructions

## Slide 4: Understanding SIMD Instructions
Implicit parallelism occur via AVX (Advanced Vector Extensions) or SSE (Streaming SIMD Instructions)
Example:
Without SIMD the following loop might be executed with four add instructions:
//Serial Loop
for(int i = 0; i < n; i+=4)
{
c[i] = a[i] + b[i]; //add c[i], a[i], b[i]
c[i+1] = a[i+1] + b[i+1]; //add c[i+1], a[i+1], b[i+1]
c[i+2] = a[i+2] + b[i+2]; //add c[i+2], a[i+2], b[i+2]
c[i+3] = a[i+3] + b[i+3]; //add c[i+3], a[i+3], b[i+3]
}

## Slide 5: Understanding SIMD Instructions
With SIMD the following loop might be executed with one add instruction:
//SIMD Loop
for(int i = 0; i < n; i+=4)
{
c[i] = a[i] + b[i]; //add c[i to i+3], a[i to i+3], b[i to i+3]
c[i+1] = a[i+1] + b[i+1];
c[i+2] = a[i+2] + b[i+2];
c[i+3] = a[i+3] + b[i+3];
}

## Slide 6: Understanding SIMD Instructions
Note that the add instructions above are pseudo-assembly instructions
The serial loop is implemented as follows:
+------+ +------+ +------+
| a[i] | + | b[i] | -> | c[i] |
+------+ +------+ +------+
+------+ +------+ +------+
|a[i+1]| + |b[i+1]| -> |c[i+1]|
+------+ +------+ +------+
+------+ +------+ +------+
|a[i+2]| + |b[i+2]| -> |c[i+2]|
+------+ +------+ +------+
+------+ +------+ +------+
|a[i+3]| + |b[i+3]| -> |c[i+3]|
+------+ +------+ +------+

## Slide 7: Understanding SIMD Instructions
Versus SIMD:
+------+ +------+ +------+
| a[i] | | b[i] | | c[i] |
| | | | | |
|a[i+1]| |b[i+1]| |c[i+1]|
| | + | | -> | |
|a[i+2]| |b[i+2]| |c[i+2]|
| | | | | |
|a[i+3]| |b[i+3]| |c[i+3]|
+------+ +------+ +------+

## Slide 8: Understanding SIMD Instructions
In the previous example 4x Speedup was achieved by using SIMD instructions
Note that SIMD Registers are often 128, 256, or 512 bits wide allowing for addition, subtraction, multiplication, etc., of 2, 4, or 8 double precision variables.
Performance of SSE and AVX Instruction Sets, Hwancheol Jeong, Weonjong Lee, Sunghoon Kim, and Seok-Ho Myung, Proceedings of Science, 2012, http://arxiv.org/pdf/1211.0820.pdf

## Slide 9: Memory Limitations
Bandwidth - rate that data can be sent from memory to the processor
Latency - for memory this could represent the amount of time to get a block of data to the CPU after a request for a word (4 or 8 bytes)
Performance effects - if memory latency is too high, it will limit what the processor can do
Imagine a 3GHz (3 cycles/nanosec) processor interacting with memory that has a 30ns latency where only one word (4 to 8 bytes) is sent at a time to the processor.
Compare to a 30ns latency where 30 words are sent to the processor at a time.

## Slide 10: Latency Improvement With Cache
Cache hit ratio - ratio of data requests satisfied by cache to total requests
Memory bound computations - computations bound by the rate at which data is sent to the CPU
Temporal Locality - data that will be used at or near the same time
  Often the same data is reused, which makes cache useful.
Example - Matrix Multiplication
  2n^3 Operations for multiplying two n by n matrices
  Data is reused, hence cache is useful, because it has a much lower latency than memory

## Slide 11: Memory Bandwidth Issues
Example
  Dot Product
  No data reuse
  Higher bandwidth is useful
Spatial Locality - data that is physically nearby (e.g. next element in a 1-D array)

## Slide 12: Memory Bandwidth Issues
Example with striding memory - Matrix addition
for(int i = 0; i < n; i++)
for(int j = 0; j < n; j++)
c[i][j] = a[i][j] + b[i][j]
vs
for(int j = 0; j < n; j++)
for(int i = 0; i < n; i++)
c[i][j] = a[i][j] + b[i][j]
Tiling - if the sections of the matrix over which we are iterating are too large, it may be useful to break the matrix into blocks and then perform the computations. This process is called tiling.

## Slide 13: Methods to Deal With Memory Latency
Prefetching - load data into cache using heuristics based upon spatial and temporal locality in the hopes that it will improve the cache miss ratio
Multithreading - run multiple threads at the same time, while waiting for data to load, we can perform processing (possibly by oversubsrcibing).
Example - n by n matrix mulitplication
for(int i = 0; i < n; i++)
for(int j = 0; j < n; j++)
for(int k = 0; k < n; k++)
c[i][j] += a[i][k]*b[k][j];
//vs
for(int i = 0; i < n; i++)
for(int j = 0; j < n; j++)
create_thread(performDotProduct(a, b, i, j,
&c[i][j]));

## Slide 14: Communications Models
Shared Address Space Model - Common data area accessible to all processors
  https://computing.llnl.gov/tutorials/parallel_comp/#Whatis
Multiprocessors (chips with multiple CPU cores) are such a platform
Multithreaded programming uses this model and is often simpler than multiprocess programming
Uniform Memory Access - time to access any memory location is equal for all CPU cores
Example - many single socket processors/motherboards - (e.g. Intel i7)
Non-uniform Memory Access - time to access memory locations varies based upon which core is used
Example - modern dual/quad socket systems (e.g. Workstations/servers/HPC)
Algorithms must build in locality and processor affinity to achieve maximum performance on such systems
For ease of programming a global address space (sometimes virtualized) is often used

## Slide 15: Cache Coherence
Cache Coherence - ensure concurrent/parallel operations on the same memory location have well defined semantics across multiple processors
  Accomplished using get and put at a native level
  May cause inconsistency across processor caches if programs are not implemented properly (i.e. if locks are not used during writes to shared variables).

## Slide 16: Synchronization Tools
Semaphores
Atomic operations
Mutual exclusion (mutex) locks
Spin Locks
TSL Locks
Condition variables and Monitors

## Slide 17: Critical Sections
Before investigating tools, we need to define critical sections
A critical section is an area of code where shared resource(s) is/are used
We would like to enforce mutual exclusion on critical sections to prevent problematic situations like two processes trying to modify the same variable at the same time
Mutual exclusion is when only one process/thread is allowed to access a shared resource while all others must wait

## Slide 18: Real Life Critical Section
| | Road B
| |
| |
Road A | |
--------+ +--------
----------> X <------ Critical
Section at X
--------+ ^ +--------
| | |
| | |
| | |
| | |

## Slide 19: Avoiding Race Conditions
The problem on the previous slide is called a race condition.
To avoid race conditions, we need synchronization.
Many ways to provide synchronization:
  Semaphore
  Mutex lock
  Atomic Operations
  Monitors
  Spin Lock
  Many more

## Slide 20: Mutual Exclusion
Mutual exclusion means only one process (thread) may access a shared resource at a time. All others must wait.
Recall that critical sections are segments of code where a process/thread accesses and uses a shared and uses a shared resource.

## Slide 21: An example where synchronization is needed
+-----------+ +---------------+
| Thread 1 | | Thread 2 |
+-----------+ +---------------+
| | | |
+-----------+ +---------------+
| x++ | | x = x * 3 |
| y = x | | y = 4 + x |
+-----------+ +---------------+
| | | |
| | | |
+-----------+ +---------------+

## Slide 22: Requirements for Mutual Exclusion
Processes need to meet the following conditions for mutual exclusion on critical sections.
Mutual exclusion by definition
Absence of starvation - processes wait a finite period before accessing/entering critical sections.
Absence of deadlock - processes should not block each other indefinitely.

## Slide 23: Synchronization Methods and Variable Sharing
busy wait - use Dekker's or Peterson's algorithm (consumes CPU cycles)
Disable interrupts and use special machine instructions (Test-set-lock or TSL, atomic operations, and spin locks)
Use OS mechanisms and programming languages (semaphores and monitors)
Variables are shared between C threads by making them global and static
Use OpenMP pragmas
  #pragma omp critical
Note that variables are shared between OpenMP threads by using
  #pragma omp parallel shared(variableName)

## Slide 24: Semaphores
Semaphore - abstract data type that functions as a software synchronization tool to implement a solution to the critical section problem
Includes a queue, waiting, and signaling functionality
Includes a counter for allowing multiple accesses
Available in both Java and C

## Slide 25: Using Semaphores
To use:
1) invoke wait on S. This tests the value of its integer attribute sem.
  If sem > 0, it is decremented and the process is allowed to enter the critical section
  Else, (sem == 0) wait suspends the process and puts it in the semaphore queue
2) Execute the critical section
3) Invoke post on S, increment the value of sem and activate the process at the head of the queue
4) Continue with normal sequence of instructions

## Slide 26: Semaphore Pseudocode
void wait()
if(sem > 0)
sem--
else
put process in the wait queue
sleep()
void post()
if (sem < maxVal)
sem++
if queue non empty
remove process from wait queue
wake up process

## Slide 27: Synchronization with Semaphores
Simple synchronization is easy with semaphores
Entry section <-- wait(&s)
Critical Section
Exit section <-- post(&s)

## Slide 28: Semaphore Example
Event ordering is also possible
Two threads P1 and P2 need to synchronize execution
P1 must write before P2 reads
//P1
write(x)
post(&s)
//P2
wait(&s)
read(x)
//s must be initialized to zero as a binary semaphore

## Slide 29: Message Passing Platforms
Message passing - transfer of data or work across nodes to synchronize actions among processes
MPI - Message passing interface - Messages passed using send/recv and processes identified by a rank
Android Services - Messages also passed using send/recv

## Slide 30: Ideal Parallel Computers
Ideal Parallel Computers - p processors and unlimited global memory uniformly accessible to all processors
  Used for modeling and theoretical purposes
Parallel Random Access Machine (PRAM) - extension of the serial random access machine
  Four classes
EREW PRAM - Exclusive read, exclusive write - no concurrent access to memory - weakest PRAM model
CREW PRAM - Concurrent read, exclusive write - concurrent access to memory for reading only
ERCW PRAM - Exclusive read, concurrent write - concurrent access to memory for writing only
CRCW PRAM - Concurrent read, concurrent write - concurrent access for both reads and writes, strongest PRAM model

## Slide 31: Ideal Parallel Computers
Protocols to resolve concurrent writes to a single memory location
Common - concurrent write allowed to one memory location if all values being writen to that location are the same
Arbitrary - one write succeeds, the rest fail
Priority - processor with the highest priority succeeds, the rest fail
Sum - sum of all results being written is written to the memory location

## Slide 32: Interconnections for Parallel Computers
Means of data transfer between processors and memory or between nodes
Can be implemented in different fashions
Static - point to point communication links (also called direct connection)
Dynamic - switches and communication links (also called indirect connection)
Degree of switch - total number of ports on a switch
Switches may provide internal buffering, routing, and multicasting

## Slide 33: Network Topologies
Bus-based networks - consists of shared interconnect common to all nodes
  Cost is linear in the number of nodes
  Distance between nodes is constant
Crossbar networks - used to connect p processors to b memory banks
  Uses a grid of switches and is non blocking
  Requires p*b switches
  Does not scale well in cost because complexity grows in the best case on the order of p^2
Multistage networks - between bus and crossbar networks in terms of cost and scalability (also called Multistage interconnection network)
  One implementation is called an Omega network (not covered)

## Slide 34: Network Topologies
Fully connected network - each node has a direct communication link to every other node
Star connected network - one node acts as a central processor and all communication is routed through that node
Linear Arrays - each node except the left-most and right-most has exactly two neighbors (for a 1D array). 2-D, 3-D, and hypercube arrays can be created to form k-dimensional meshes.
Tree-Based Network - only one path exists between any pair of nodes
  Routing requires sending a message up the tree to the smallest sub-tree that contains both nodes
  Since tree networks suffer from communication bottlenecks near the root of the tree, a fat tree topology is often used to increase bandwidth near the root

## Slide 35: Static Interconnection Networks
Diameter - maximum distance between any pair of processing nodes
  Diameter of a ring network is floor(p/2)
  Diameter of a complete binary tree is 2 * log( (p+1)/2 )
  p is the number of nodes in the system
Connectivity - multiplicity of paths between processing nodes
Arc Connectivity - number of arcs that must be removed to break the network into two disconnected networks
  One for a star topology, two for a ring
Bisection Width - number of links that must be removed to break the network into two equal halves
Bisection Bandwidth - minimum volume of communication allowed between any two halves of the network

## Slide 36: Static Interconnection Networks
Channel width - bits that can be communicated simultaneously over a link connecting two nodes. Equivalent to number of physical wire in each communication link.
Channel rate - peak rate a wire can deliver bits
Channel bandwidth - peak rate that data can be communicated between ends of a communication link
Cross-section bandwidth - another name for bisection bandwidth
Cost evaluation/criteria - number of communication links, number of wires
Similar criteria exist to evaluate dynamic networks (i.e. those including switches)

## Slide 37: Cache Coherence in Multiprocessor Systems
May need to keep multiple copies of data consistent across multiple processors
But multiple processors may update data
For shared variables, the coherence mechanism must ensure that operations on the shared data are serializable
Other copies of the shared data must be invalidated and updated
For memory operations, shared data that will be written to memory must be marked as dirty
False sharing – different processors update different parts of the same cache line

## Slide 38: Maintaining Cache Coherence
Snooping
  Processors are on a broadcast interconnect implemented by a bus or ring
  Processors montor the bus for transactions
  Bus acts as a bottleneck for such systems
Directory Based Systems
  Maintain a bitmap for cache blocks and their associated processors
  Maintain states (invalid, dirty, shared) for each block in use
  Performance varies depending upon implementation (distributed vs. shared)

## Slide 39: Communication Methods and Costs
Message Passing Costs
  Startup time (latency) – time to handle a message at sending and receiving nodes (e.g. adding headers, establishing an interface between the node and router, etc.)
    One time cost
  Per-hop time – time to reach the next node in the path
  Per word transfer time – time to transfer 1 word including buffering overhead
Message Passing Methods
  Store and Forward Routing
  Packet Routing
  Cut through routing (Preferred)
  Prefer to force message packets to take the the same route for parallel computing and for messages to be broken into small pieces

## Slide 40: Rules for Sending Messages
Optimization of message passing is actually quite simple and includes the following rules:
Communicate in bulk
Minimize volume of data
Minimize distance of data transfer
It is possible to determine a cost model for message passing

## Slide 41: Communication Costs in Shared Address Spaces
Difficult to model because layout is determined by system
Cache thrashing is possible
Hard to quantify overhead for invalidation and update operations across cache
Hard to model spatial locality
Prefetching can reduce overhead and is hard to model
False sharing can cause overhead
Resource contention can also cause overhead